## Slide 1: Solution:
Tri-Protos: UART + I2C + SPI

## Slide 2: Solution Uart
1: Open the capture file.
2: Section containing the captured frames.
3: Click here to add protocole (UART)
1
2
3

## Slide 3: Solution Uart
4: Search UART and click on
5: Open menu, a settings are:
  RX: D0
  TX: D1
  Baud rate: 9600
  Data bits: 8
  Parity: None
  Stop bits: 1.0
  Bit order: lsb-fist
  Data format: ASCII
4
5

## Slide 4: Solution Uart
Zoom on largest tram
4
5

## Slide 5: Solution I2C
1: Open the capture file.
2: Section containing the captured frames.
3: Click here to add protocole (I2C)
1
3
3
2

## Slide 6: Solution I2C
Like UART, put D0 on SCL and SDA on D1

## Slide 7: Solution I2C
In DW case, you have flag. But there is second option.

## Slide 8: Solution I2C
1: click on down arrow and choose « Binary decoder output view»
2: Choose data write
3: part of flag is here
1
2
3